## Slide 1: Tele Convergence
Anowar Hasan Sabir, Suman Kumar Saha, Al Faruq Ibna Nazim, Jahangir Hossain

## Slide 2: AGENDA
Architecture & Benefits
Case Study
Key Findings

## Slide 3
BACKGROUND

## Slide 4: BACKGROUND : The Beginning
An organization with a headquarter located centrally which had 15+ zonal areas and had more than 150+ branches located remotely with zones.
What do they have and practice:
They have a central internet connectivity.
They had zones connected with E1.
They had a central IP-PBX soft switch.
They had application systems, mailing etc. running centrally.
Had PABX for inter-telecommunication and PSTN dropped to call out and have calls in for all places.

## Slide 5: BACKGROUND : Realization
Having communication through Datacom.
Having independent system for zones to be operational even if data link unavailable
Having PSTN to be trunked to remote locations.
Having PABX lines to be trunked to few locations.
So they asked for
MUX for all locations.
Routers to integrate with data & MUX.
PABX unit for independent dialer.
Microwave setups for connectivity.

## Slide 6: BACKGROUND : Realization
Complexity !!!
Expensive !!!
Mess !!!
Burden !!!
…….

## Slide 7: BACKGROUND : Realization
My Proposal
Packet switching.
Layer-3 network for connectivity nodes.
Single box solution.
Integrated communication equipment.
Complexity minimization.

## Slide 8
ARCHITECTURE & BENEFITS

## Slide 9: Considering Scenarios
Nationwide distributed work areas.
Implemented legacy PABX for internal communication.
Data & Internet connectivity.
Single box solution.
Area with lower resources considering rural area and environment.

## Slide 10: Common Organization Scenario

## Slide 11: Transformation Scenario 1

## Slide 12: Transformation Scenario 2

## Slide 13
CASE SCENARIO: A Nationwide Spread Organization
1XXX
3XXX
2XXX
40XX
41XX
42XX
43XX
50XX
51XX
52XX
53XX
60XX
61XX
62XX
63XX
70XX
71XX
72XX
73XX
80XX
81XX
82XX
83XX
90XX
91XX
92XX
93XX

## Slide 14
CASE SCENARIO:
Actual Network
Diagram

## Slide 15
CASE SCENARIO:
Zone 1
Network
Diagram

## Slide 16
CASE SCENARIO:
Zone 2
Network
Diagram

## Slide 17: Why Such integration?
Using the customers existing circuit setup PABX or PSTN.
Using cross site communication.
Using packet communication for connectivity.
Going ahead in advanced communication technology.
Cost benefit while transforming technology.

## Slide 18
CASE STUDY

## Slide 19: CASE STUDY: A sample Lab for such scenario
Prime Integrations:
Asterisk Server.
Cisco Routers.
Legacy PABX integration.
PSTN connectivity integration.

## Slide 20: CASE STUDY: Asterisk Server Configuration
vi /etc/asterisk/extensions.conf
[cme-trunk]
Exten => _X.,1,Set(do_Voicemail=no)
Exten => _X.,n,NoOp(${CALLERID(num)})
Exten => _X.,n,Dial(SIP/${EXTEN})
Exten => _X.,n,NoOp(${HANGUPCAUSE} DAN ${DIALSTATUS})
Exten => _X.,n,Hangup()
;###Router01###
Exten => _20XX.,1,Set(do_Voicemail=no)
Exten => _20XX.,n,NoOp(${CALLERID(num)})
Exten => _20XX.,n,Dial(SIP/Router01/${EXTEN},,tTw)
Exten => _20XX.,n,NoOp(${HANGUPCAUSE} DAN ${DIALSTATUS})
Exten => _20XX.,n,Hangup()
;###Router02###
Exten => _21XX.,1,Set(do_Voicemail=no)
Exten => _21XX.,n,NoOp(${CALLERID(num)})
Exten => _21XX.,n,Dial(SIP/Router02/${EXTEN},,tTw)
Exten => _21XX.,n,NoOp(${HANGUPCAUSE} DAN ${DIALSTATUS})
Exten => _21XX.,n,Hangup()
vi /etc/asterisk/sip.conf
[Router01]
type=friend
host=10.11.121.2
dtmfmode=rfc2833
relaxdtmf=yes
canreinvite=no
insecure=port,invite
context=cme-trunk
quality=yes
nat=yes
Disallow=all
Allow=ulaw
Allow=alaw
[Router02]
type=friend
host=10.11.121.6
dtmfmode=rfc2833
relaxdtmf=yes
canreinvite=no
insecure=port,invite
context=cme-trunk
quality=yes
nat=yes
Disallow=all
Allow=ulaw
Allow=alaw
Context “cme-trunk”actually allows the router peer configurations at sip.conf file. As for router01 information in sip.conf it gives informations for peering router like IP, codec etc. As when the dial pattern needed the use each other simultaneously. As for router01 dial pattern you can find that it is seeking Router01 name from sip.conf
Notes: Context “cme-trunk”actually allows the router peer configurations at sip.conf file. As for router01 information in sip.conf it gives informations for peering router like IP, codec etc. As when the dial pattern needed the use each other simultaneously. As for router01 dial pattern you can find that it is seeking Router01 name from sip.conf

## Slide 21: CASE STUDY: Cisco Router Configuration ( Basic Configuration for voice )
voice service voip // Declaring the voice service over which mode. In our case its IP.
allow-connections h323 to h323
allow-connections h323 to sip
allow-connections sip to h323
allow-connections sip to sip
supplementary-service h450.12 advertise-only // Common Information Additional Network Feature for H.323
fax protocol t38 ls-redundancy 0 hs-redundancy 0 fallback pass-through g711ulaw // Declaring fax protocol enabling low and high signal and giving option if fax protocol not available to go through an audio codec
sip // sip configuration
rel1xx disable // Reliable provisional response support disabled to stop error code
registrar server expires max 1200 min 60 // Enabling SIP registry server and mentioning its expire time
!
voice class codec 1 // declaring a codec group tag
codec preference 1 g711ulaw
codec preference 2 g711alaw
!
voice register global // Global registry information declaration
mode cme // mode defining to CME of Cisco
source-address 10.11.121.2 port 5060 // Defining a registry server IP and port
max-dn 10 // maximum dial no defining
max-pool 10 // maximum pool defining
tftp-path flash: // configuration loaded from flash with tftp
create profile sync 0004028852090405 // Creating profile for IP phones
!
ccm-manager application redundant port 5060 // Call manager application redundant port declaration
!
dspfarm profile 1 transcode universal // Digital Signal Processor (DSP) profile for codec transformation for IP to IP media gateway
description Transcoding
codec g711ulaw
codec g711alaw
maximum sessions 5
associate application SCCP
!
sip-ua // SIP user agent informations
registrar ipv4:10.11.121.2 expires 3600
sip-server ipv4:10.11.121.2
!
telephony-service // CUCME configuration for router
max-ephones 10
max-dn 10
system message #Router01#
time-zone 21
max-conferences 8 gain -6
transfer-system full-consult
!
Notes: voice service voip // Declaring the voice service over which mode. In our case its IP.
allow-connections h323 to h323
allow-connections h323 to sip
allow-connections sip to h323
allow-connections sip to sip
supplementary-service h450.12 advertise-only // Common Information Additional Network Feature for H.323
fax protocol t38 ls-redundancy 0 hs-redundancy 0 fallback pass-through g711ulaw // Declaring fax protocol enabling low and high signal and giving option if fax protocol not available to go through an audio codec
sip // sip configuration
rel1xx disable // Reliable provisional response support disabled to stop error code
registrar server expires max 1200 min 60 // Enabling SIP registry server and mentioning its expire time
!
voice class codec 1 // declaring a codec group tag
codec preference 1 g711ulaw
codec preference 2 g711alaw
!
voice register global // Global registry information declaration
mode cme // mode defining to CME of Cisco
source-address 10.11.121.2 port 5060 // Defining a registry server IP and port
max-dn 10 // maximum dial no defining
max-pool 10 // maximum pool defining
tftp-path flash: // configuration loaded from flash with tftp
create profile sync 0004028852090405 // Creating profile for IP phones
!
ccm-manager application redundant port 5060 // Call manager application redundant port declaration
!
dspfarm profile 1 transcode universal // Digital Signal Processor (DSP) profile for codec transformation for IP to IP media gateway
description Transcoding
codec g711ulaw
codec g711alaw
maximum sessions 5
associate application SCCP
!
sip-ua // SIP user agent informations
registrar ipv4:10.11.121.2 expires 3600
sip-server ipv4:10.11.121.2
!
telephony-service // CUCME configuration for router
max-ephones 10
max-dn 10
system message #Router01#
time-zone 21
max-conferences 8 gain -6
transfer-system full-consult
!

## Slide 22: CASE STUDY: Cisco Router Configuration ( Registering IP Phone / Pots Phone / Voice peer )
voice register dn 1 // Dial number declaration
number 2001
allow watch
name 2001
!
voice register pool 1 // Pool profile information for the number
id mac 0030.4F7B.E3F9
number 1 dn 1
dtmf-relay sip-notify
username 2001 password 123456
codec g711ulaw
no vad
!
dial-peer voice 1 pots // POTS number declaration
destination-pattern 2002
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 voip // Peering with asterisk server
description Router01-Asterisk
destination-pattern 1...
session protocol sipv2
session target ipv4:10.11.120.100:5060
dtmf-relay sip-notify
codec g711ulaw
no vad
!
dial-peer voice 3 voip // Peering with routers
description Router01-Router02
destination-pattern 21..
session protocol sipv2
session target ipv4:10.11.121.6:5060
dtmf-relay sip-notify
codec g711ulaw
no vad
Notes: voice register dn 1 // Dial number declaration
number 2001
allow watch
name 2001
!
voice register pool 1 // Pool profile information for the number
id mac 0030.4F7B.E3F9
number 1 dn 1
dtmf-relay sip-notify
username 2001 password 123456
codec g711ulaw
no vad
!
dial-peer voice 1 pots // POTS number declaration
destination-pattern 2002
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 voip // Peering with asterisk server
description Router01-Asterisk
destination-pattern 1...
session protocol sipv2
session target ipv4:10.11.120.100:5060
dtmf-relay sip-notify
codec g711ulaw
no vad
!
dial-peer voice 3 voip // Peering with routers
description Router01-Router02
destination-pattern 21..
session protocol sipv2
session target ipv4:10.11.121.6:5060
dtmf-relay sip-notify
codec g711ulaw
no vad

## Slide 23: CASE STUDY: Legacy PABX integration
!
dial-peer voice 1 pots
preference 1
destination-pattern 2000
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 pots
preference 2
destination-pattern 2000
incoming called-number .%
port 0/0/1
!
dial-peer voice 3 pots
preference 3
destination-pattern 2000
incoming called-number .%
port 0/0/2
!
dial-peer voice 4 pots
preference 4
destination-pattern 2000
incoming called-number .%
port 0/0/3
!

## Slide 24: CASE STUDY: PSTN Connectivity Integration ( Call in/out for PSTN if considered legacy PBX)
!
voice-port 0/3/1
connection plar opx 2000
description PSTN-FXO-Router1-PABX 029117891
caller-id enable
!
voice-port 0/3/2
connection plar opx 2000
description PSTN-FXO-Router1-PABX 029117892
caller-id enable
!
!
dial-peer voice 1 pots
description PSTN-Out
destination-pattern 0T
direct-inward-dial
forward-digits all
port 0/3/1
!
dial-peer voice 2 pots
description PSTN-Out
destination-pattern 0T
direct-inward-dial
forward-digits all
port 0/3/2
!
An incoming call to the PSTN numbers are forwarded to 2000
Call out numbers beginning with 0
Through PSTN ports

## Slide 25: CASE STUDY: PSTN Connectivity Integration ( Call in/out for PSTN if considered legacy PBX)
!
voice-port 0/3/1
connection plar opx 2000
description PSTN-FXO-Router1-PABX 029117891
caller-id enable
!
voice-port 0/3/2
connection plar opx 2000
description PSTN-FXO-Router1-PABX 029117892
caller-id enable
!
!
dial-peer voice 1 pots
description PSTN-Out
destination-pattern 0T
direct-inward-dial
forward-digits all
port 0/3/1
!
dial-peer voice 2 pots
description PSTN-Out
destination-pattern 0T
direct-inward-dial
forward-digits all
port 0/3/2
!
This will create a loop circuit for which all ports will be off-hook.
This will allow all to use outgoing through PSTN

## Slide 26: CASE STUDY: PSTN Connectivity Integration ( Call in for PSTN if considered legacy PBX)
In such case its better if we use hunt group for PABX integration
!
voice hunt-group 1 sequential
list 2097, 2098, 2099
timeout 15
pilot 2000
!
dial-peer voice 1 pots
destination-pattern 2097
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 pots
destination-pattern 2098
incoming called-number .%
port 0/0/1
!
dial-peer voice 3 pots
destination-pattern 2099
incoming called-number .%
port 0/0/2
!

## Slide 27: CASE STUDY: PSTN Connectivity Integration ( Dedicated PSTN and using it for remote router)
Call in for Router1 ( Resided in Router2)
!
voice-port 0/3/1
connection plar opx 2010
description PSTN-FXO-Router1-PABX 029117891
caller-id enable
!
voice-port 0/3/2
connection plar opx 2012
description PSTN-FXO-Router1-PABX 029117892
caller-id enable
!
Call out for Router1 ( Resided in Router1)
!
voice translation-rule 1
rule 1 /^0/ /A20100/
!
voice translation-rule 2
rule 1 /^0/ /A20120/
!
voice translation-profile phone2010
translate called 1
!
voice translation-profile phone2012
translate called 2
!
voice register dn 1
translation-profile incoming phone2010
number 2010
allow watch
name 2010
!
!
dial-peer voice 1 pots
translation-profile incoming phone2012
destination-pattern 2012
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 voip
description PSTN-OUT-2010
destination-pattern A2010T
session protocol sipv2
session target ipv4:10.11.121.2
dtmf-relay sip-notify
codec g711ulaw
no vad
!
dial-peer voice 3 voip
description PSTN-OUT-2012
destination-pattern A2012T
session protocol sipv2
session target ipv4:10.11.121.2
dtmf-relay sip-notify
codec g711ulaw
no vad
!
Call out for Router1 ( Resided in Router2)
dial-peer voice 1 pots
description Call-Out-For-2010
destination-pattern A2010T
direct-inward-dial
port 0/3/0
!
dial-peer voice 2 pots
description Call-Out-For-2012
destination-pattern A4202T
direct-inward-dial
port 0/3/1

## Slide 28: CASE STUDY: PSTN Connectivity Integration ( Dedicated PSTN and using it for remote router)
Call in for Router1 ( Resided in Router2)
!
voice-port 0/3/1
connection plar opx 2010
description PSTN-FXO-Router1-PABX 029117891
caller-id enable
!
Call out for Router1 ( Resided in Router1)
!
voice translation-rule 1
rule 1 /^0/ /A20100/
!
voice translation-profile phone2010
translate called 1
!
dial-peer voice 1 pots
translation-profile incoming phone2012
destination-pattern 2012
incoming called-number .%
port 0/0/0
!
dial-peer voice 2 voip
description PSTN-OUT-2010
destination-pattern A2010T
session protocol sipv2
session target ipv4:10.11.121.2
dtmf-relay sip-notify
codec g711ulaw
no vad
!
!
Call out for Router1 ( Resided in Router2)
!
dial-peer voice 1 pots
description Call-Out-For-2010
destination-pattern A2010T
direct-inward-dial
port 0/3/0
!

## Slide 29: CASE STUDY: Remote FXO activity due to local device or data network failure
The FXO port will be offhook and no connection can be established other than port reset. So the following should be maintained for FXO ports.
Reasons:
While we disconnect lines through phone a tone is recognized to reset the port to tell that it should be onhook to establish calls.
Each country uses their own tones to perform this operation.
So just like circuit connectivity Packet connectivity is required to carry its actual tone to destination port to tell it to onhook for link breakage.
For a help we can try the following site where custom tones are listed by country usage.
http://www.3amsystems.com/World_Tone_Database
Notes: Reasons:
While we disconnect lines through phone a tone is recognized to reset the port to tell that it should be onhook to establish calls.
Each country uses their own tones to perform this operation.
So just like circuit connectivity Packet connectivity is required to carry its actual tone to destination port to tell it to onhook for link breakage.
For a help we can try the following site where custom tones are listed by country usage.
http://www.3amsystems.com/World_Tone_Database

## Slide 30: CASE STUDY: Remote FXO activity due to local device or data network failure
voice class dualtone-detect-params 1
freq-max-deviation 20
cadence-variation 20
!
voice class custom-cptone BD-CPTONE
dualtone disconnect
frequency 450
cadence 200 300 700 800 3000 10000 250
!
voice-port 0/3/1
supervisory disconnect dualtone mid-call
supervisory custom-cptone BD-CPTONE
supervisory dualtone-detect-params 1
compand-type a-law
cptone GB
timeouts call-disconnect 1
timeouts wait-release 1
connection plar opx 2010
description PSTN-FXO-Router1-PABX 029117891
caller-id enable
!
voice-port 0/3/2
supervisory disconnect dualtone mid-call
supervisory custom-cptone BD-CPTONE
supervisory dualtone-detect-params 1
compand-type a-law
cptone GB
timeouts call-disconnect 1
timeouts wait-release 1
connection plar opx 2012
description PSTN-FXO-Router1-PABX 029117892
caller-id enable
!

## Slide 31: Conclusion: Final Achievements and Future
A distributed organization can operate on their own communication pattern.
While merging to this technology their existing legacy technology PABX is integrated.
Zone based registry allows you to have you own area communication due to unavailability of data connection.
Local or remote PSTN integration.
Scope generated due to implementation
FAX integration or personal FAX network.
Achieving a single area of communication management for voice, video, data, internet etc.
Achieving IP-PABX smart features.
Using data communication more efficiently sharing it with QOS.
Getting IP-TSP trunks as an alternative option of PSTN.